## Slide 1
 TCP/IP stands for Transmission Control Protocol/Internet
Protocol
 so named for two of its most important protocols
 Internet Protocol Suite
 (the phrase used in official Internet standard documents)
 one of the available network protocol* suites
 (*protocol – formal description of a set of rules and conventions that govern how devices on a network exchange information)
3
What is TCP/IP?

## Slide 2
4
Why TCP/IP?
 The de facto standard for computer communications in today’s networked world
 The world’s most popular open system (nonproprietary)
 they can be used to communicate across any set of interconnected networks
 equally well suited for LAN and WAN communications
 The “engine” for the Internet!

## Slide 3
 An internet under TCP/IP operates like a single network connecting many computers of various sizes and types
 The Internet is an interconnection of independent physical networks (e.g. LANs) linked together by internetworking devices (i.e routers/gateways)
 The main task of the Internet and its TCP/IP protocol suite is to provide services for users
5
TCP/IP and the Internet

## Slide 4
6
TCP/IP and the Internet

## Slide 5
 TCP/IP is not the only network protocol
 Other Protocols:
 NETBEUI – IBM PC/MS Windows
 IPX – Novell NetWare
 AppleTalk – Apple Macintosh
 SNA – IBM Mainframes
 DECnet – Digital Equipments
 etc.
7
TCP/IP versus other Network
Protocols

## Slide 6
 Like most network protocols, TCP/IP is a layered protocol
 each layer builds upon the layer below it, adding new functionality
 normally compared to Open Systems Interconnection (OSI)* reference model to better understand the functions of each layer
 (*OSI is a conceptual framework for communications between computer and network devices; defined by ISO)
8
OSI Reference Model and TCP/IP

## Slide 7
9
OSI Reference Model

## Slide 8
 Each layer defines a family of functions (or services) distinct from those of the other layers
 modular, comprehensive, flexible
 The OSI model allows complete transparency between otherwise incompatible systems
 A mnemonic for remembering the layers
•
Please Do Not Touch Steve’s Pet Alligator
Physical, Data link, Network, Transport, Session, Presentation,
Application (1 to 7)
Pupils Should Treat Nice Lecturer Properly!
Application, Presentation, Session, Transport, Network, data Link,
Physical (7 to 1)
10
OSI Model – Layered Architecture

## Slide 9
11
OSI Model – Summary of Layers

## Slide 10
12
Relationship of Layers and
Addresses in TCP/IP

## Slide 11
 Nodes are connected by a link; at the data link level the frame contains physical addresses
 Most LAN uses 48-bit (6 bytes) physical address,
 e.g. 07-01-02-01-2C-4B (written as 12 hexadecimal digit)
13
Physical Address

## Slide 12
 Physical addresses are not adequate in an internetwork environment – a universal addressing system in which each host can be identified uniquely, regardless of the underlying physical network
 IP address (32 bits)
 e.g. 132.24.75.9 (written as four decimal number)
14
Internet Address

## Slide 13
15
Internet Address

## Slide 14
 multiple processes may be
running at the same time
 port addresses differentiate the communicating processes
 in TCP/IP a port address is represented by one decimal number
 e.g. 80 (common port for HTTP)
16
Port Address

## Slide 15
 Static
 Dynamic
17
IP Addressing (Internet Address)

## Slide 16
 You have to go to each individual device
 Meticulous records must be kept
 No duplicate IP addresses
18
Static IP Addressing

## Slide 17
 Dynamic Host Configuration Protocol (DHCP)
 Successor to BOOTP
 Allows host to obtain an IP address quickly and dynamically
 Uses a defined range of IP address
 Reverse Address Resolution Protocol (RARP)
 Binds MAC addresses to IP addresses
 BOOTstrap Protocol (BOOTP)
 Uses UDP to carry messages
 Uses broadcast IP datagram
 MAC address pre-matched to IP address
 Can contain additional information (default gateway)
19
Dynamic Addressing

## Slide 18
20
DHCP

## Slide 19
21
DHCP – Getting more than the IP Address

## Slide 20
22
RARP

## Slide 21
23
Dumb Terminals

## Slide 22
RARP Broadcast: I know
my MAC address, but what is my IP address?
RARP Server Unicast:
Here is your IP address.
24
RARP reply

## Slide 23
 BOOTP (Bootstrap Protocol)
 Provides IP address, subnet mask, default gateway IP address and DNS IP address.
Disadvantage:
 BOOTP is not a dynamic configuration protocol (like DHCP).
 When a client requests an IP address the BOOTP server looks up its MAC address in a table to find the IP address.
 This binding is predetermined.
 What if the computer is moved to another subnet/network?
 Use DHCP!
25
BOOTP

## Slide 24
26
ARP

## Slide 25
Source host does not know the MAC address of the destination.
ARP request frame is a broadcast to all MAC address
All devices on the local segment will investigate the frame to check if their own IP address matches the destination IP address.
ME?
27
IP Header
Destination
192.168.1.100
Source
192.168.1.205
ARP

## Slide 26
 If no – discard the packet
 If yes:
 Reads rest of packet
 Returns ARP reply
 ARP reply
 Supplies
MAC
address
of the
host.
no
no
Hey –my IP matches
Source: Arp Request
My
MAC
address
28
ARP

## Slide 27
29
The ARP Table

## Slide 28
 For Microsoft Windows hosts:
 Initial mappings have a 2-minute time-to-live.
 An entry that is used twice in 2 minutes is automatically given a 10- minute time-to-live.
 For Unix/Linux hosts:
 Initial mappings have a 20 minute time-to-live.
30
Aging Out

## Slide 29
Similarities
Both are concerned with mapping IP to MAC addresses
Both use same packet format
Both use broadcast addresses for their task.
Differences
 ARP - obtains MAC address of other clients by using an IP address while RARP – obtains its own (local host) IP address by using its own (local host’s) MAC address
 ARP packets are broadcast on local network by using broadcast MAC address (ff-ff-ff- ff-ff-ff) while RARP uses broadcast IP address (255.255.255.255) as well as broadcast MAC address (ff-ff-ff-ff-ff-ff)
 ARP table maintained by local host while RARP table maintained by RARP server
 ARP reply is used by local host to update its ARP table and to send packets to destination while RARP reply is used to configure the IP protocol of a local host.
31
Compare ARP & RARP

## Slide 30
198.189.232.1
32
Using a default gateway

## Slide 31
 Many times we communicate with other hosts using domain
names such as www.nwu.edu.ng
 Hosts and routers route packets using IP addresses, NOT
domain names.
 The
 The
 The
host must translate the domain name to an IP address.
host will have the DNS Server do this translation for it. Domain Name System (abbreviated DNS) is an Internet
directory service.
 DNS is how domain names are translated into IP addresses, and DNS also controls email delivery.
 If your computer cannot access DNS, your web browser will not be able to find web sites, and you will not be able to receive or send email.
33
Domain Names and IP Addresses

## Slide 32
34

## Slide 33
We usually use domain names,
www.cisco.com, but the IP packets are sent using the IP address, 198.133.219.25.
198.133.219.25
35
Domain Names and IP Addresses

## Slide 34
How it works
 A DNS server is just a computer that's running DNS software.
 Since most servers are Unix machines, the most popular program is BIND (Berkeley Internet Name Domain), but you can find software for the Mac and the PC as well.
36
Exploring the Domain Name Space

## Slide 35
 DNS software is generally
made up of two elements: the actual name server, and something called a resolver.
 The name server responds to browser requests by supplying name-to-address conversions.
 When it
answer, another
doesn't know the
the resolver will ask name server for the
information.
37
Exploring the Domain Name Space

## Slide 36
 To see how it works, let's go
back to the domain-name- space inverted tree.
 When you type in a URL, your browser sends a request to
the closest name server.
 If that server has ever fielded a request for the same host name (within a time period
set by the administrator to prevent passing old information), it will locate the information in its cache and reply.
38
Exploring the Domain Name Space

## Slide 37
 If the name server unfamiliar with the domain name, the resolver is attempt to solve the problem by asking further up the tree
 If that doesn't work, the second server will ask yet another - until it finds one that knows.
 (When a server can supply an answer without asking another, it's known as an authoritative server.)
39
Exploring the Domain Name Space

## Slide 38
 Once the information is located, it's passed back to your
browser.
 Usually this process occurs quickly, but occasionally it can take an excruciatingly long time (like 15 seconds).
40
Exploring the Domain Name Space

## Slide 39
In the worst cases, you'll get a dialog box that says the domain name doesn't exist - even though you know it does.
This happens because the authoritative server is slow replying to the first, and your computer gets tired of waiting so it times-out (drops the connection).
But if you try again, there's a good chance it will work, because the authoritative server has had enough time to reply, and your name server has stored the information in its cache.
41
Exploring the Domain Name
Space

## Slide 40
The End
42